## Slide 1
Design Project (PVL292)
M.Tech VLSI Design
ASSERTION-BASED VERIFICATION OF
SYNCHRONOUS FIFO USING
SYSTEMVERILOG
Submitted by
Kapil Tripathi
6025620017
Under supervision of
Dr. Arnab Pattanayak
Dr. Lalit Kumar Baghel
Electronics and Communication Engineering Department
Thapar Institute of Engineering & Technology, Patiala
May 2026
SystemVerilog + SVA + Scoreboard + Fault Injection

## Slide 2
Presentation Roadmap
Project flow
Assertion-Based Verification of Synchronous FIFO
02
1
Problem and objective
Why FIFO control must be verified before reuse.
2
DUT architecture
Synchronous FIFO with separate RAM and controller.
3
SV environment
Generator, driver, monitor, scoreboard, and interface.
4
SVA plan
Assertions bound to internal FIFO control signals.
5
Fault results
Five injected issues with waveform/log evidence.
6
Conclusion
Findings, limitations, and UVM migration path.
The deck follows the same logic as the report, but keeps each result focused on what failed, which checker caught it, and what the waveform proves.

## Slide 3
Why FIFO Verification Matters
Motivation
Assertion-Based Verification of Synchronous FIFO
03
A FIFO is simple in concept but sensitive at its boundaries: reset, empty, full, read/write overlap, and pointer wrap.
Data ordering
Oldest accepted write must be the first valid read. A pointer bug can silently repeat or skip stored data.
Flow control
full and empty are not cosmetic flags. They directly block writes and reads to prevent overflow and underflow.
Reset safety
The FIFO must start from a known empty state so later traffic is not contaminated by stale count or pointer values.
Debug observability
Assertions expose internal control mistakes immediately, while the scoreboard checks visible data behavior.
Producer
FIFO
queue
Consumer

## Slide 4
Why SystemVerilog Over Verilog
Language choice
Assertion-Based Verification of Synchronous FIFO
04
SystemVerilog keeps Verilog-style RTL, but adds verification features that are directly useful for this FIFO project.
Verilog HDL
- Strong fit for synthesizable RTL modeling
- Modules, nets, registers, always blocks
- Basic procedural testbenches are possible
- Limited language support for reusable verification
- Assertions, classes, coverage, and constrained random are not the core Verilog model
SystemVerilog
- Unified design, specification, and verification language
- Assertions for protocol and temporal properties
- Classes, mailboxes, and virtual interfaces for testbench reuse
- Constrained random stimulus and functional coverage support
- Natural foundation for later UVM migration
IEEE 1800-2023 describes SystemVerilog support for RTL/gate modeling and testbenches using coverage, assertions, object-oriented programming, and constrained random verification.

## Slide 5
Synchronous FIFO Basics
DUT behavior
Assertion-Based Verification of Synchronous FIFO
05
First-in first-out rule
The FIFO accepts writes into the tail and reads from the head. Status flags are generated from occupancy count.
Write side
wr_en
wr_data
wr_ptr advances
FIFO storage
oldest data at front
fifo_count tracks occupancy
full / empty from count
Read side
rd_en
rd_data
rd_ptr advances
Key control equations
do_write = wr_en && !full;
do_read = rd_en && !empty;
full = (fifo_count == DEPTH);
empty = (fifo_count == 0);
Project parameters
DW = 8 data bits
AW = 4 address bits
DEPTH = 2^AW = 16 entries
fifo_count range = 0..16

## Slide 6
Design Under Test Architecture
sync_fifo_ram + sync_ram
Assertion-Based Verification of Synchronous FIFO
06
The verified DUT separates control from storage: sync_fifo_ram manages pointers/count/flags, while sync_ram stores data.
Inputs
clk, rst
wr_en, rd_en
wr_data
FIFO controller
wr_ptr, rd_ptr
fifo_count
do_write, do_read
full, empty
Synchronous RAM
waddr, raddr
din, dout
write enable
Outputs
rd_data
full
empty
Bound SVA checker
observes internal pointers, count, and accepted operations
Scoreboard model
keeps expected FIFO order using a queue

## Slide 7
SystemVerilog Verification Environment
Class-based testbench
Assertion-Based Verification of Synchronous FIFO
07
The environment separates stimulus generation, bus driving, monitoring, and result checking. This makes each failure easier to localize.
Generator
random
transaction
Driver
drives
fifo_if
Interface
clk/rst
signals
DUT
sync_fifo_ram
SVA
bind checker
Monitor
samples bus
Scoreboard
compares expected
vs actual data
SystemVerilog features used
class-based transaction, randomized generator, mailbox communication, virtual interface, bind-based assertions

## Slide 8
Assertion-Based Verification Plan
SVA checker
Assertion-Based Verification of Synchronous FIFO
08
Assertions observe internal controller state and state exactly what must be true after each accepted operation.
RST_STATE
After reset: empty high, full low, pointers zero, count zero
FULL_FLAG / EMPTY_FLAG
Flags must match fifo_count == DEPTH and fifo_count == 0
COUNT_RANGE
fifo_count must stay within 0..DEPTH
WRITE_ONLY
write pointer increments, read pointer stable, count increments
READ_ONLY
read pointer increments, write pointer stable, count decrements
READ_WRITE
both pointers move while count remains stable
READ_EMPTY / WRITE_FULL
invalid requests must be blocked at boundaries
Example property intent
READ_ONLY:
(!do_write && do_read) |=>
wr_ptr == $past(wr_ptr) &&
rd_ptr == $past(rd_ptr) + 1'b1 &&
fifo_count == $past(fifo_count) - 1'b1;

## Slide 9
Fault Injection Methodology
Negative testing
Assertion-Based Verification of Synchronous FIFO
09
Five faulty RTL copies were tested one at a time. The clean testbench and assertion module stayed unchanged.
1
Start clean
Run clean design and confirm zero errors
2
Insert one fault
Copy one buggy design into EDA Playground design.sv
3
Run simulation
Keep testbench.sv and assert_fifo_ram.sv fixed
4
Capture evidence
Save transcript failures and EPWave waveform
Issue 1
Reset count not cleared
Issue 2
Read accepted while empty
Issue 3
Full flag asserted too early
Issue 4
Empty flag asserted one count early
Issue 5
Read pointer does not advance

## Slide 10
Baseline Expected Behaviour
Clean RTL
Assertion-Based Verification of Synchronous FIFO
10
Before negative testing, the clean FIFO must satisfy normal state transitions and boundary blocking rules.
0
expected scoreboard errors for clean run
16
FIFO depth when AW = 4
5
intentional faulty RTL versions
SVA
structural/protocol checks
Reset
wr_ptr = 0, rd_ptr = 0, fifo_count = 0, empty = 1
Write-only
wr_ptr increments and fifo_count increases
Read-only
rd_ptr increments and fifo_count decreases
Simultaneous read/write
both pointers move and fifo_count stays stable
Boundary rules
read blocked when empty; write blocked when full
Pointer update example
Correct RTL target:
rd_ptr <= rd_ptr + 1'b1;
Issue 5 bug changes this to:
rd_ptr <= rd_ptr;

## Slide 11
Fault Results: Issues 1 and 2
Reset and underflow protection
Assertion-Based Verification of Synchronous FIFO
11
Issue 1: reset count not cleared
Bug: fifo_count reset to 1 instead of 0.
Caught by: RST_STATE assertion.
Effect: empty flag becomes wrong immediately after reset.
Issue 2: read while empty
Bug: do_read uses rd_en without checking empty.
Caught by: READ_EMPTY and COUNT_RANGE.
Effect: fifo_count underflows and rd_data becomes invalid.
Issue 1 waveform: fifo_count starts at 1 during reset
Issue 1 log: reset assertion failures
Issue 2 waveform: do_read accepted while empty
Issue 2 log: READ_EMPTY, unknown data, count range

## Slide 12
Fault Result: Issue 3
Full flag asserted too early
Assertion-Based Verification of Synchronous FIFO
12
Bug inserted
assign full = (fifo_count == 1);
Correct: full should assert only when fifo_count == DEPTH.
Observed failure
At fifo_count = 1, the DUT reports full even though 15 locations remain available.
Checker response
FULL_FLAG assertion compares the flag against fifo_count == DEPTH and fails repeatedly.
Waveform: full asserted when fifo_count is one
Simulation log: repeated FULL_FLAG assertion failures
Interpretation: this bug does not necessarily corrupt data immediately, but it destroys usable FIFO capacity and blocks valid writes too early.

## Slide 13
Fault Result: Issue 4
Empty flag asserted one count early
Assertion-Based Verification of Synchronous FIFO
13
Bug inserted
assign empty = (fifo_count == 1);
Correct: empty should assert only when fifo_count == 0.
Observed failure
The DUT reports empty while one valid FIFO entry still remains.
Checker response
EMPTY_FLAG assertion fails because empty no longer represents the true count-zero condition.
Waveform: empty high while fifo_count equals one
Simulation log: EMPTY_FLAG assertion failures
Interpretation: status flag correctness is part of functional correctness because empty directly controls whether reads are accepted.

## Slide 14
Fault Result: Issue 5
Read pointer does not advance
Assertion-Based Verification of Synchronous FIFO
14
Real affected RTL file
rtl/sync_fifo_ram.sv
The selected write-side code is correct; the fault is in the read pointer update.
Issue 5 code focus
Bug:
if (do_read) begin
rd_ptr <= rd_ptr;
end
Correct:
rd_ptr <= rd_ptr + 1'b1;
Effect
Valid reads are accepted and fifo_count changes, but rd_ptr remains fixed. The FIFO repeatedly reads the same RAM address.
Waveform: rd_ptr remains fixed while reads occur
Simulation log: READ_ONLY assertion and data mismatch
Assertion localizes the internal pointer failure; scoreboard confirms the visible FIFO-order failure.

## Slide 15
Comparative Result Summary
Assertions + scoreboard
Assertion-Based Verification of Synchronous FIFO
15
Issue
Fault injected
Primary assertion
Scoreboard effect
Conclusion
1
fifo_count not cleared on reset
RST_STATE
Queue/data mismatch later
reset state bug
2
do_read ignores empty
READ_EMPTY, COUNT_RANGE
Data mismatch after underflow
boundary bug
3
full high at count 1
FULL_FLAG
False full messages
capacity loss
4
empty high at count 1
EMPTY_FLAG
False empty messages
valid reads blocked
5
rd_ptr stuck during reads
READ_ONLY
Expected order breaks
pointer/data bug
Pattern: assertions catch control/protocol violations at the exact clocked condition; the scoreboard catches externally visible data-order consequences.

## Slide 16
Key Findings and Contribution
What the project demonstrates
Assertion-Based Verification of Synchronous FIFO
16
The project demonstrates that assertion-based verification improves observability beyond transaction-level checking alone.
1. Assertions localize failures
Internal signals such as wr_ptr, rd_ptr, fifo_count, do_write, and do_read are checked at the clock where the rule is violated.
2. Scoreboard validates behavior
The queue-based reference model confirms whether the output data still follows FIFO order after control faults.
3. Waveforms explain timing
EPWave evidence connects assertion timestamps to signal transitions, making root cause analysis clear.
Main contribution
A parameterized synchronous FIFO was verified with a SystemVerilog class-based environment, bound SVA checker, scoreboard, and five intentional negative tests. The result is a reusable verification base that can be extended toward UVM.

## Slide 17
Conclusion, Future Work, and References
Close
Assertion-Based Verification of Synchronous FIFO
17
Conclusion
The clean FIFO behavior was established first. Each injected RTL fault produced assertion or scoreboard failures, proving that the environment can detect reset, boundary, flag, pointer, and data-order bugs.
Future improvements
Migrate to UVM agents and sequences.
Add functional coverage bins for full/empty transitions.
Add constrained random regression tests.
Add coverage-driven closure and CI simulation scripts.
References
1. IEEE SA, IEEE 1800-2023: SystemVerilog - Unified Hardware Design, Specification, and Verification Language.
2. Accellera, Universal Verification Methodology community and standards pages.
3. Local project report: TIET_Assertion_Based_FIFO_Verification_Report.docx.
4. Project source files: rtl/sync_fifo_ram.sv, rtl/sync_ram.sv, tb/assert_fifo_ram.sv, tb/*.svh.
5. Simulation evidence: EPWave and transcript screenshots from images/issue1 through images/issue5.
Final message: SVA gives precise internal failure localization; the scoreboard proves whether the design still obeys FIFO data ordering.